# GetUp Design Document

## Requirements
### Functional

### Power

## Power Calculations
### Known values
Power source used is two LR44 button cell. The specifications for this battery are [1]:
  - Nominal voltage: 1.5 V
  - Capcity: 105 mAh (1.5 V to 1.1 V)
  - Internal resistance: < 20 ohm
  - Weight: 1.75 g
Atmega328p power usage:
@ 3.3 V @ 8 Mhz – 6.6 mA (TODO test again)
@ 3.3 V @ xxx ohm – 4.0 mA (TODO test)
### Calculations
Assume there are four LEDs. Assume the LEDs flash at 1 Hz. Assume the on time for the LEDs is 30 ms. Assume the LEDs flash for on average 1 minute (both get up and sit down flash combined).
LED power usage:
4 (LEDs) x 0.030 s (on time) x 1 Hz (rate) x 60 s (flashing time) x 0.004 A (current)
= 0.0288 As = 28.8 mAs = 0.008 mAh
Assume chip is running only while LEDs are flashing, otherwise it is sleeping. The chip can only sleep for up to 8 seconds at a time, so must wake up to go back to sleep. Assume that the additional power usage to wake up is negligible.
ATmega328p on usage:
60 s x 0.0066 A
= 0.395 As = 395 mAs = 0.1097 mAh
ATmega328p sleep usage.
(3600 s – 60 s) x 0.000010 A
= 0.0354 As = 35.4 mAs = 0.009833 mAh
Total hourly power usage:
0.008 mAh + 0.1097 mAh + 0.009833 mAh
= 0.1275 mAh per hour
6 % LED, 7 % sleep usage, 87 % running usage.
Conclusion, sleeping while the LEDs are flashing will provide a significant power saving.
105 mAh / 0.1275 mAh
= 823.5 hours = 137 days @ 6 hours per day.
## References
 [1] http://www.farnell.com/datasheets/11186.pdf